## Slide 1: X-ray Photoelectron Spectroscopy ——Application in Phase-switching Device Study
Xinyuan Wang
A53073806

## Slide 2: Outline
Background
Basic Principles
XPS Instruments
Data Analysis
Application in Reference Paper

## Slide 3: Background
XPS, based on photoelectric effect, was first explained by Albert Einstein
During the mid 1960’s Dr. Siegbahn and his research group developed the XPS technique

## Slide 4: Outline
Background
Basic Principles
XPS Instruments
Data Analysis
Application in Reference Paper

## Slide 5: Basic Principles
X-rays
  Irradiate the sample surface, hitting the core electrons (e-) of the atoms
  Penetrate the sample to a depth on the order of a micrometer
  Useful emission electron signal is obtained only from a depth of around 10 to 100 Å on the surface
  The X-Ray source produces photons with either certain energies, known as monoenergetic X-ray beam
    MgK photon with an energy of 1253.6 eV
    AlK photon with an energy of 1486.6 eV

## Slide 6: Basic Principles
electron emission when transfer energy is greater than the electron’s binding energy
Photon

## Slide 7: Outline
Background
Basic Principles
XPS Instruments
Data Analysis
Application in Reference Paper

## Slide 8: Instrument
The technique is widely used because it is very simple to use and the data is easily analyzed
Commonly the system has three main modules
  An X-ray source
  An electron energy analyzer
  A detection system

## Slide 9: Instrument
Ultra High Vacuum (UHV) environment
  all the three modules are contained in a vacuum chamber
  Signal of emitted electrons will decrease with residual gas molecules
  Surface sensitivity of XPS
The Sample
  be stable in a vacuum chamber
  sample size amenable to the instrument
  surface of sample remains clean before and during analysis
X-ray Sources
  high energy anode materials with small line width
  provide depth profiling capability

## Slide 10: Outline
Background
Basic Principles
XPS Instruments
Data Analysis
Application in Reference Paper

## Slide 11: Data Analysis
XPS Survey Spectrum
  a wide scan over a region that provide strong peaks for all elements
  identify elements present
    XPS peaks are sharp
    large C 1s resulting from the deposition of adventitious carbon from the atmosphere

## Slide 12: Data Analysis
Followed up by spectra around the elemental peaks of interest
Depth Profiling
  etch and analyze

## Slide 13: Data Analysis
Depth Profiling
  concentration of different elements versus depth within 10nm
Application in Reference paper

## Slide 14: Data Analysis
Chemical Shift
  small changes in electron energy regarding to chemical environment of the emitting element
  computer curve fitting of high-resolution XPS spectra

## Slide 15: Data Analysis
Similar process in reference paper

## Slide 16: Thank you!